## Slide 1
SMART INDIA HACKATHON 2026 | PS ID: SIH26173
VaaniSetu (वाणी सेतु)
AI-Powered Voice Bridge for Ultra-Low-Bitrate & Weak Radio/Network Links
98% Bandwidth Slashed
Reduces required voice bandwidth from 24,000+ bps down to 60–300 bps (300–800 bits per sentence).
Pure Voice-In / Voice-Out
Zero typing or screen reading. Natural voice is captured, compressed as semantic tokens, and regenerated as speech.
Cross-Lingual Calling
Direct Indic-to-Indic translation (IndicTrans2) between Hindi, Tamil, Telugu, and English in-flight.

## Slide 2
VAANISETU | SIH 2026
The Problem: Digital Voice Collapse in Austere & Disaster Zones
🚨 Critical Communications Failure
• In disaster relief, border operations, and maritime zones, cellular 4G/5G and broadband collapse entirely.
• Emergency HF/VHF radio, satellite, and LoRa networks are capped at 300 to 2,400 bps.
• Standard digital codecs (Opus, AMR, G.711) demand 12,000 to 64,000 bps—making voice calls physically impossible.
• Result: Total loss of real-time voice contact when it is needed most.
🛑 Why Existing Alternatives Fail
• Text / SMS is Unusable: Field operatives, drivers, and rescue teams cannot look down or type in high-stress, tactical environments.
• Vocoders (MELP/Codec2) Break Down: Compressing sound waves below 2.4 kbps produces robotic, muffled, unintelligible audio.
• Severe Language Barriers: Inter-state rescue squads struggle to coordinate across regional Indian languages during emergencies.
• The Solution: We must retain natural voice while transmitting 100x less data.

## Slide 3
VAANISETU | SIH 2026
The Paradigm Shift: Semantic Transmission over Waveform Compression
❌ Conventional Approach (Signal Compression)
• Attempts to compress the acoustic waveform harder and harder.
• Transmits heavy acoustic data: 12,000 – 64,000 bits per second.
• Requires 120,000+ bits for a simple 5-second sentence.
• Chokes and drops completely on weak 300–2400 bps emergency links.
• Audio artifacts destroy intelligibility under radio noise.
✅ VaaniSetu Approach (Semantic Transmission)
• Discards the acoustic carrier; extracts and transmits semantic meaning.
• Transmits error-corrected text tokens: only 60 – 300 bits per second.
• Requires only 300 – 800 bits total for a 5-second sentence (98% reduction).
• Re-synthesizes high-fidelity, natural human speech at the receiver.
• 100% Voice-In, Voice-Out: The user only ever hears and speaks audio.

## Slide 4
VAANISETU | SIH 2026
End-to-End Technical Pipeline
1. Ingestion & Translation
• Capture: 16 kHz Mono PCM via Push-to-Talk (PTT).
• STT: AI4Bharat IndicConformer / IndicWav2Vec regional speech model.
• NMT: AI4Bharat IndicTrans2 direct Indic-to-Indic translation (no English pivot).
2. Compression & FEC
• Deflate Compression: Level-9 zlib payload shrinking.
• Binary Framing: Custom big-endian header (Lang Tag + Payload length).
• Reed-Solomon FEC: 10 parity symbols protect both payload & headers against bit noise.
3. Transmission & Synthesis
• Transport: 300–2400 bps simulated or hardware link (LoRa / HF / VHF).
• Zero-Hallucination Gate: Strict mathematical error recovery; flags lost packets.
• Edge TTS: High-fidelity regional neural voice output (Tamil, Telugu, Hindi).

## Slide 5
VAANISETU | SIH 2026
Channel Engineering: Binary Wire Protocol & Reed-Solomon FEC
📦 Custom Binary Wire Protocol
• Eliminates bloated JSON/HTTP overhead (which wastes 150+ bytes per word).
• Wire Struct: [1B Lang Len] + [NB Lang Tag] + [4B Payload Len] + [MB Compressed Payload]
• Header Overhead: Only 5 to 7 bytes total.
• Total Packet Size: Under 40–100 bytes for standard spoken sentences.
🛡️ Reed-Solomon Forward Error Correction
• Configured over Galois Field GF(2^8) with 10 error-correction symbols.
• Mathematical Correction: Restores up to t = floor(ECC/2) = 5 corrupted bytes per packet without retransmission.
• Full-Frame Wrapping: RS parity wraps the entire frame (headers + payload).
• Zero Hallucination Contract: When noise exceeds correction threshold, packet is cleanly flagged as lost (lost: true). Never guesses or fabricates words.

## Slide 6
VAANISETU | SIH 2026
Bandwidth Benchmark: 98% Data Reduction
Parameter | Standard VoIP (G.711 / Opus) | Low-Bitrate Vocoder (MELP) | VaaniSetu Voice Bridge
Required Bitrate | 12,000 – 64,000 bps | 2,400 bps | 60 – 300 bps
Data per 5s Sentence | 120,000 – 320,000 bits | 12,000 bits | 300 – 800 bits
Works over 300 bps Link? | ❌ Fails Completely | ❌ Severe Distortion | ✅ Flawless Operation
Cross-Lingual Support? | ❌ None | ❌ None | ✅ Native Indic Translation
Bandwidth Savings | Baseline (0%) | 80% – 90% | 97.5% – 99.1% (40x–100x)
Key Takeaway: By eliminating waveform transmission, VaaniSetu operates comfortably inside HF/VHF and LoRa channels where VoIP fails completely.

## Slide 7
VAANISETU | SIH 2026
Uniqueness & Core Differentiators (USPs)
USP #1: 40x–100x Data Reduction
Reduces voice budget from 120,000 bits to <800 bits per sentence.
USP #2: Speak Mine, Hear Yours
Native IndicTrans2 enables Hindi, Tamil, Telugu, and English real-time cross-talk.
USP #3: Zero Screen UI
Pure voice-in and voice-out preserves situational awareness in emergency zones.
USP #4: Defense-Grade Reliability
Reed-Solomon FEC + zero-hallucination contract strictly flags corrupted packets.

## Slide 8
VAANISETU | SIH 2026
Current Status & Working Prototype
✅ Tested & Functional Modules
• 22 Unit & Integration Tests Passing (test_channel_roundtrip, test_stt, test_tts, test_translation, test_websocket).
• FastAPI Orchestrator (:8000) with full room-pairing & language negotiation.
• React Native Mobile App with PTT audio recording & live bit-budget telemetry.
• Standalone pre-built signed Android APK (VaaniSetu-final.apk) ready on device.
🚀 Deployment & Extension Roadmap
• Hardware Transceiver Coupling: Direct plug-in for SX1262 LoRa modules and HackRF / RTL-SDR.
• On-Device NPU Acceleration: Quantized (ONNX/GGUF) edge inference to run fully offline on ruggedized handsets.
• Mesh Protocol Relay: Multi-hop relaying for isolated mountain and maritime rescue groups.
• Field Deployment: Defense border outposts & NDRF disaster response teams.